| Table A-10 Permeable Pavement BMPs |
| --- |
| Variable Use columns to the right to compute runoff volume retention from proposed permeable pavement BMPs | DA | DA | DA |
| 1 Infiltration rate of underlying soils (in/hr) See Section 5.4.2 and Appendix D of the TGD for WQMP for minimum requirements for assessment methods |  |  |  |
| 2 Infiltration safety factor See Section 5.4.2 and Appendix D of the TGD for WQMP |  |  |  |
| 3 Design percolation rate (in/hr): Pdesign = Item 1 / Item 2 |  |  |  |
| 4 Infiltrating surface area, SABMP (ft2) |  |  |  |
| 5 Gravel depth, dmedia (ft) |  |  |  |
| 6 Gravel porosity |  |  |  |
| 7 Duration of storm as basin is filling (hrs) Typical ~ 3hrs |  |  |  |
| 8 Retention Volume (ft3): Vretention = Item 4 * [ (Item 5 * Item 6) + (Item 7 * (Item 3 / 12)] |  |  |  |