| Table A-1 LID BMP Performance Criteria for Design Capture Volume Drainage Area |
| --- |
| 1 Drainage area (ft2): | 2 Imperviousness after applying preventative site design practices (Imp%): | 3 Runoff Coefficient (Rc): Rc = 0.858(Imp%)^3-0.78(Imp%)^2+0.774(Imp%)+0.04 |
| 4 Determine 1-hour rainfall depth for a 2-year return period P2yr-1hr (in): http://hdsc.nws.noaa.gov/hdsc/pfds/sa/sca_pfds.html |
| 5 Compute P6, Mean 6-hr Precipitation (inches): P6 = Item 4 *C1, where C1 is a function of site climatic region specified in Table 3-2 of the TGD for WQMP (Valley = 1.4807; Mountain = 1.909; Desert = 1.2371) |
| 6 Drawdown Rate Use 48 hours unless site has soils with average field-measured permeability greater than 2 inches/hr. The necessary BMP footprint is a function of drawdown time. While shorter drawdown times reduce the performance criteria for LID BMP design capture volume, the depth of water that can be stored is also reduced, therefore larger BMP footprints may be needed to capture smaller design capture volume in sites with soil permeability less than 2 in/hr. | 24-hrs ( 48-hrs ( |
| 7 Compute design capture volume VDCV (ft3): VSDCV = 1/12 * [Item 1* Item 3 *Item 5 * C2], where C2 is a function of drawdown rate (24-hr = 1.582; 48-hr = 1.963) Compute separate VDCV for each DA to a roadway inlet |

| Table A-2 Summary of HCOC Assessment Drainage Area |
| --- |
| Does project have the potential to cause or contribute to an HCOC in a downstream channel: Yes ( No ( Go to: http://sbcounty.permitrack.com/WAP/ If "Yes", then complete HCOC assessment of site hydrology for 2 yr storm event using Tables A-3 through A-5 and insert results below. Tables A-3 through A-5 may be replaced by computer software analysis that is based on the San Bernardino County Hydrology Manual. Complete separate HCOC assessment for each DA to a roadway inlet If “No,” then proceed to Form A-6 |
| Condition | Runoff Volume (ft3) | Time of Concentration (min) | Peak Runoff (cfs) |
| Pre-developed | 1 Table A-3, Item 8 | 2 Table A-4, Item 13 | 3 Table A-5, Item 6pre-developed |
| Post-developed | 4 Table A-3, Item 9 | 5 Table A-4, Item 14 | 6 Table A-5, Item 6 post-developed |
| Difference | 7 Item 4 – Item 1 | 8 Item 2 – Item 5 | 9 Item 6 – Item 3 |
| Difference (as % of pre-developed) | 10 % Item 7 / Item 1 | 11 % Item 8 / Item 2 | 12 % Item 9 / Item 3 |

| Table A-3 HCOC Assessment for Runoff Volume Drainage Area |
| --- |
| Variables Complete separate HCOC assessment for each DA to a roadway inlet | Pre-developed DA | Post-developed DA |
| 1 Land cover |  |  |
| 2 Hydrologic Soil Group |  |  |
| 3 Drainage Area (ft2) Sum of DAs should equal total site area (Form 2-2) |  |  |
| 4 Curve Number (CN) Use Items 1 and 2 to select curve number from TGD for WQMP Appendix C-2 |  |  |
| 5 Pre-developed soil storage capacity, S (in): S = 1000 / Item 4 - 10 |  |  |
| 6 Pre-developed initial abstraction, Ia (in): Ia = 0.2 * Item 5 |  |  |
| 7 Precipitation for 2 yr, 24 hr storm (in): Go to: http://hdsc.nws.noaa.gov/hdsc/pfds/sa/sca_pfds.html |
| 8 Pre-developed volume (ft3): Vpre =(1 / 12) * (Item 3) * [(Item 7 – Item 6)^2 / (Item 7 – Item 6 + Item 5)] |
| 9 Post-developed volume (ft3): Vpost = (1 / 12) * (Item 3) * [(Item 7 – Item 6)^2 / (Item 7 – Item 6 + Item 5)] |
| 10 Volume Reduction Needed to meet HCOC Requirement (ft3): VHCOC = (Item 9 * 0.95) – Item 8 |

| Table A-4 HCOC Assessment for Time of Concentration Drainage Area |
| --- |
| Compute time of concentration for pre and post developed conditions (For projects using the Hydrology Manual complete the form below) |
| Variables | Pre-developed DA | Post-developed DA |
| 1 Length of flowpath (ft) Use Form 3-2 Item 5 for pre-developed condition |  |  |
| 2 Change in elevation (ft) |  |  |
| 3 Slope (ft/ft) So = Item 2 / Item 1 |  |  |
| 4 Land cover |  |  |
| 5 Initial DA Time of Concentration (min) TGD for WQMP Appendix C-1 |  |  |
| 6 Length of conveyance from DA outlet to project site outlet (ft) For post-developed condition, use length of linear BMP receiving runoff from the DA |  |  |
| 7 Cross-sectional area of channel / gutter / swale (ft2) |  |  |
| 8 Wetted perimeter of channel / gutter / swale (ft) |  |  |
| 9 Manning’s roughness of channel / gutter / swale (n) |  |  |
| 10 Flow velocity (ft/sec): Vfps = (1.49 / Item 9) * (Item 7/Item 8)^0.67 * (Item 3)^0.5 |  |  |
| 11 Travel time to outlet (min): Tt = Item 6 / (Item 10 * 60) or if BMP is not a swale or linear bioretention, then provide the hydraulic retention time |  |  |
| 12 Total time of concentration (min): Tc = Item 5 + Item 11 |  |  |
| 13 Pre-developed time of concentration (min): |
| 14 Post-developed time of concentration (min): |
| 15 Additional time of concentration needed to meet HCOC requirement (min): TC-HCOC = (Item 13 * 0.95) – Item 14 |

| Table A-5 HCOC Assessment for Peak Runoff Drainage Area |
| --- |
| Compute peak runoff for pre and post developed conditions. (For projects using the Hydrology Manual complete the form below) |
| Variables Complete separate HCOC assessment for each DA to a roadway inlet | Pre-developed DA | Post-developed DA |
| 1 Rainfall Intensity for storm duration equal to time of concentration: Ipeak = 10^(LOG Form A-2 Item 4 - 0.7 LOG Form A-5 Item 5 + 1.067) |  |  |
| 2 Drainage Area (Acres) |  |  |
| 3 Ratio of pervious area to total area |  |  |
| 4 Pervious area infiltration rate (in/hr) Use pervious area CN and antecedent moisture condition with TGD for WQMP Appendix C-3 |  |  |
| 5 Maximum loss rate (in/hr): Fm = Item 2 * Item 3 |  |  |
| 6 Peak Flow from DA (cfs): Qp =Item 2 * 0.9 * (Item 1 - Item 5) |  |  |
| 7 Peak runoff reduction needed to meet HCOC Requirement (cfs): Qp-HCOC = (Item 6post-developed * 0.95) – Item 6pre-developed |